Pan version 3.0

© 2001 - 2007 Pentaho

http://www.pentaho.org

Table of contents

# Pan
## Panとは?
Panは、XMLファイルまたはリポジトリに保管されたデータ変換を実行するプログラムです。通常、データ変換はバッチ・モードで自動的に実行されます。

## インストール
あらかじめJRE（Java Runtime Enviroment）バージョン1.4以上をインストールしてください。JREのダウンロードサイトは http://www.java.com/ を参照してください。

その後、Kettle-3.0.zip（圧縮形式ファイル）を導入先のディレクトリで解凍してください。
UNIX環境（Solaris, Linux, OSX, ...）の場合は、追加タスクとして、次の例にしたがってシェルスクリプトに実行権限を付与してください。

cd Kettle
chmod +x *.sh

## Panの実行
Panを実行するためには、それぞれの環境で以下のスクリプトを実行してください。

- Pan.bat:	Windows環境
- pan.sh:	UNIX環境（Solaris, Linux, OSX, ...）

## コマンドのオプション
コマンドのオプションについて説明します。

IMPORTANT NOTES:
- On Windows system, the use of the minus (“-”) in the options causes problems as well as the equal sign (“=”). Because of this, from version 2.2.2 on, you can also use this format or any combination of /,- and :,=
- Fields in italic represent the values that the options use.
- It’s important that if spaces are present in the option values, you use quotes or double quotes to keep them together. Take a look at the examples below for more info.
/option:value

有効なオプション

バージョン情報の表示

-version

このオプションは Kettle コアライブラリ (kettle.jar) のバージョンを表示します。
作成した最新のバージョン番号およびバージョン日付が表示されます。

XMLファイルの指定

-file=filename

このオプションはデータ変換が定義された XML file. (.ktr : Kettle Transformation) を指定します。

ログファイルの指定

-log=Logging Filename

実行時のログファイルを指定します。デフォルトは標準出力です。

ロギングレベルの指定

-level=Logging Level

このオプションはログファイルのロギングレベルを指定します。
次のロギングレベルが選択できます。

- Error:	エラーのみを出力
- Nothing:	何も出力しない
- Minimal:	最小レベルのログを出力
- Basic:	標準レベルのログを出力
- Detailed:	詳細レベルのログを出力
- Debug:	デバッグレベル（より詳細な）のログを出力
- Rowlevel:	行レベルのログを出力

リポジトリの指定

-rep=Repository name

接続するリポジトリの名前 (“Repository name”) を指定します。
このオプションを指定した場合は、さらに追加オプションとして –user, –pass および –trans を指定しなければなりません。
このオプションを環境変数として指定する場合は、次の環境変数名を指定してください。
 KETTLE_REPOSITORY.

ユーザー名の指定

-user=Username

接続するリポジトリのユーザー名を指定します。
このオプションを環境変数として指定する場合は、次の環境変数名を指定してください。
KETTLE_USER.

パスワードの指定

-pass=Password

接続するリポジトリのパスワードを指定します。
このオプションを環境変数として指定する場合は、次の環境変数名を指定してください。KETTLE_PASSWORD.

データ変換名の指定

-trans=Transformation Name

リポジトリから実行するデータ変換名を指定します。

リポジトリディレクトリの表示

-listdir=Y

オプション “-dir” で指定されたリポジトリディレクトリのサブディレクトリを含むすべてのディレクトリを表示します。

リポジトリディレクトリの指定

-dir=directory

使用するリポジトリディレクトリを指定します。
ルートディレクトリ:	　　　 /
サブディレクトリ（絶対パス）:	/production/Dimensions

データ変換名の表示

-listtrans=Y

オプション “-dir” で指定されたリポジトリディレクトリ含まれるすべてのデータ変換名を表示します。

使用可能なリポジトリの表示

-listrep=Y

使用可能なすべてのリポジトリを表示します。

リポジトリのエクスポート

-exprep=filename.xml

このオプションはリポジトリ情報をファイル（ XML file.）に出力します。
このファイルはリポジトリのリストアに使用します。 Spoon または Chef のリポジトリエクスプローラで使用してください。詳しい内容は、 Spoon または Chef のマニュアルを参照してください。

リポジトリ接続の抑制

-norep=Y

このオプションを指定した場合は、リポジトリへの接続を行いません。

## パス
サンプルを実行する前にKettleディレクトリに移動してください。

Windows環境の場合：

D:
cd \Kettle

UNIX環境の場合：

cd /product/Kettle/

## ファイルからデータ変換を実行する例
Windows環境の場合：

pan.bat /file:”D:\Transformations\Customer Dimension.ktr” /level:Basic

UNIX環境の場合：

pan.sh –file=“/PRD/Customer Dimension.ktr” –level=Minimal

## リポジトリからデータ変換を実行する例
Windows環境の場合：

pan.bat /rep:“Production Repository”
        /trans:”update Customer Dimension”
 /dir:/Dimensions
        /user:matt
        /pass:somepassword123
        /level:Basic

## 標準出力
実行すると経過はスクリーン上に標準出力として表示されます。この内容をファイルに出力したい場合は、次の例にしたがってリダイレクションを使用してください。

UNIX環境の場合：

pan.sh –file=“/PRD/trans.ktr” –level=Minimal >> /LOG/trans.log

Windows環境の場合：

pan.bat /file:C:\PRD\trans.ktr /level:Basic > C:\LOG\trans.log

## 戻りコード
Pan から実行時に生成される戻りコードについて説明します。

0	正常終了
1	データ変換を処理中にエラーが発生しました。
2	予期せぬエラーが発生しました。
3	データ変換の初期化ができません。
7	データ変換がファイルまたはリポジトリからロードできません。
8	ステップのプラグインがロードできません。
9	コマンドラインの引数が違います。

# スケジュール
## Windows環境でのスケジュール
Windows環境でスケジュールを設定する方法はDOSプロンプト上でatコマンドを使用して設定する方法とGUIのコントロールパネルから設定する方法の２種類があります。
以下の例は、DOSプロンプト上でatコマンドを使用して設定する方法を示しています。

at 23:30 /every:Monday,Wednesday,Friday "D:\update_dimensions.bat"

スケジュールを確認する場合は以下のコマンドを入力してください。

at

## UNIX環境でのスケジュール
まず最初にデータ変換を実行するためのシェルスクリプトを作成してください。
それを次にcrontabコマンドを使用してスケジュールを設定します。

crontab –e

crontabコマンドでは、次のパラメータを指定してください。

- 分:	分を指定します。（範囲：0-59）
- 時:	時を指定します。（範囲：0-23）
- 日:	日を指定します。（範囲：1-31）
- 月:	月を指定します。（範囲：1-12）
- 週:	週を指定します。（範囲：0-6, 0=日曜日）

２つの値をハイフン（-）で連結した場合はその値の範囲で実行します。複数の値をカンマ（,）で区切って指定した場合はその値の時に実行します。アスタリスク（*）を指定した場合はそのパラメータを無視します。各パラメータの間はスペースで区切ってください。

次の例は、毎時15分と45分に月曜日から金曜日の範囲で実行するスケジュールを示しています。

#
# Launches the update of the dimensions in the warehouse
#
15,45 * * * 1-5 /PROD/update_dimensions.sh
#

# ライセンス
## Short version
Starting with version 2.2.0 Kettle is released into the public domain under the LGPL license.
Please refer to the complete text of this license in the next paragraph.

Copyright (C) 2007 Pentaho Corporation
   Kettle is free software; you can redistribute it and/or
   modify it under the terms of the GNU Lesser General Public
   License as published by the Free Software Foundation; either
   version 2.1 of the License, or (at your option) any later version.
   Kettle is distributed in the hope that it will be useful,
   but WITHOUT ANY WARRANTY; without even the implied warranty of
   MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU
   Lesser General Public License for more details.
   You should have received a copy of the GNU Lesser General Public
   License along with the Kettle distribution; if not, write to the Free Software
   Foundation, Inc., 51 Franklin St, Fifth Floor, Boston, MA 02110-1301 USA
## Complete text

 GNU LESSER GENERAL PUBLIC LICENSE
      Version 2.1, February 1999
Copyright (C) 1991, 1999 Free Software Foundation, Inc.
    51 Franklin St, Fifth Floor, Boston, MA 02110-1301 USA
Everyone is permitted to copy and distribute verbatim copies
of this license document, but changing it is not allowed.
[This is the first released version of the Lesser GPL. It also counts
as the successor of the GNU Library Public License, version 2, hence
the version number 2.1.]
   Preamble
 The licenses for most software are designed to take away your
freedom to share and change it. By contrast, the GNU General Public
Licenses are intended to guarantee your freedom to share and change
free software--to make sure the software is free for all its users.
 This license, the Lesser General Public License, applies to some
specially designated software packages--typically libraries--of the
Free Software Foundation and other authors who decide to use it. You
can use it too, but we suggest you first think carefully about whether
this license or the ordinary General Public License is the better
strategy to use in any particular case, based on the explanations below.
 When we speak of free software, we are referring to freedom of use,
not price. Our General Public Licenses are designed to make sure that
you have the freedom to distribute copies of free software (and charge
for this service if you wish); that you receive source code or can get
it if you want it; that you can change the software and use pieces of
it in new free programs; and that you are informed that you can do
these things.
 To protect your rights, we need to make restrictions that forbid
distributors to deny you these rights or to ask you to surrender these
rights. These restrictions translate to certain responsibilities for
you if you distribute copies of the library or if you modify it.
 For example, if you distribute copies of the library, whether gratis
or for a fee, you must give the recipients all the rights that we gave
you. You must make sure that they, too, receive or can get the source
code. If you link other code with the library, you must provide
complete object files to the recipients, so that they can relink them
with the library after making changes to the library and recompiling
it. And you must show them these terms so they know their rights.
 We protect your rights with a two-step method: (1) we copyright the
library, and (2) we offer you this license, which gives you legal
permission to copy, distribute and/or modify the library.
 To protect each distributor, we want to make it very clear that
there is no warranty for the free library. Also, if the library is
modified by someone else and passed on, the recipients should know
that what they have is not the original version, so that the original
author's reputation will not be affected by problems that might be
introduced by others.
 Finally, software patents pose a constant threat to the existence of
any free program. We wish to make sure that a company cannot
effectively restrict the users of a free program by obtaining a
restrictive license from a patent holder. Therefore, we insist that
any patent license obtained for a version of the library must be
consistent with the full freedom of use specified in this license.
 Most GNU software, including some libraries, is covered by the
ordinary GNU General Public License. This license, the GNU Lesser
General Public License, applies to certain designated libraries, and
is quite different from the ordinary General Public License. We use
this license for certain libraries in order to permit linking those
libraries into non-free programs.
 When a program is linked with a library, whether statically or using
a shared library, the combination of the two is legally speaking a
combined work, a derivative of the original library. The ordinary
General Public License therefore permits such linking only if the
entire combination fits its criteria of freedom. The Lesser General
Public License permits more lax criteria for linking other code with
the library.
 We call this license the "Lesser" General Public License because it
does Less to protect the user's freedom than the ordinary General
Public License. It also provides other free software developers Less
of an advantage over competing non-free programs. These disadvantages
are the reason we use the ordinary General Public License for many
libraries. However, the Lesser license provides advantages in certain
special circumstances.
 For example, on rare occasions, there may be a special need to
encourage the widest possible use of a certain library, so that it becomes
a de-facto standard. To achieve this, non-free programs must be
allowed to use the library. A more frequent case is that a free
library does the same job as widely used non-free libraries. In this
case, there is little to gain by limiting the free library to free
software only, so we use the Lesser General Public License.
 In other cases, permission to use a particular library in non-free
programs enables a greater number of people to use a large body of
free software. For example, permission to use the GNU C Library in
non-free programs enables many more people to use the whole GNU
operating system, as well as its variant, the GNU/Linux operating
system.
 Although the Lesser General Public License is Less protective of the
users' freedom, it does ensure that the user of a program that is
linked with the Library has the freedom and the wherewithal to run
that program using a modified version of the Library.
 The precise terms and conditions for copying, distribution and
modification follow. Pay close attention to the difference between a
"work based on the library" and a "work that uses the library". The
former contains code derived from the library, whereas the latter must
be combined with the library in order to run.
 GNU LESSER GENERAL PUBLIC LICENSE
  TERMS AND CONDITIONS FOR COPYING, DISTRIBUTION AND MODIFICATION
 0. This License Agreement applies to any software library or other
program which contains a notice placed by the copyright holder or
other authorized party saying it may be distributed under the terms of
this Lesser General Public License (also called "this License").
Each licensee is addressed as "you".
 A "library" means a collection of software functions and/or data
prepared so as to be conveniently linked with application programs
(which use some of those functions and data) to form executables.
 The "Library", below, refers to any such software library or work
which has been distributed under these terms. A "work based on the
Library" means either the Library or any derivative work under
copyright law: that is to say, a work containing the Library or a
portion of it, either verbatim or with modifications and/or translated
straightforwardly into another language. (Hereinafter, translation is
included without limitation in the term "modification".)
 "Source code" for a work means the preferred form of the work for
making modifications to it. For a library, complete source code means
all the source code for all modules it contains, plus any associated
interface definition files, plus the scripts used to control compilation
and installation of the library.
 Activities other than copying, distribution and modification are not
covered by this License; they are outside its scope. The act of
running a program using the Library is not restricted, and output from
such a program is covered only if its contents constitute a work based
on the Library (independent of the use of the Library in a tool for
writing it). Whether that is true depends on what the Library does
and what the program that uses the Library does.
 1. You may copy and distribute verbatim copies of the Library's
complete source code as you receive it, in any medium, provided that
you conspicuously and appropriately publish on each copy an
appropriate copyright notice and disclaimer of warranty; keep intact
all the notices that refer to this License and to the absence of any
warranty; and distribute a copy of this License along with the
Library.
 You may charge a fee for the physical act of transferring a copy,
and you may at your option offer warranty protection in exchange for a
fee.
 2. You may modify your copy or copies of the Library or any portion
of it, thus forming a work based on the Library, and copy and
distribute such modifications or work under the terms of Section 1
above, provided that you also meet all of these conditions:
   a) The modified work must itself be a software library.
   b) You must cause the files modified to carry prominent notices
   stating that you changed the files and the date of any change.
   c) You must cause the whole of the work to be licensed at no
   charge to all third parties under the terms of this License.
   d) If a facility in the modified Library refers to a function or a
   table of data to be supplied by an application program that uses
   the facility, other than as an argument passed when the facility
   is invoked, then you must make a good faith effort to ensure that,
   in the event an application does not supply such function or
   table, the facility still operates, and performs whatever part of
   its purpose remains meaningful.
   (For example, a function in a library to compute square roots has
   a purpose that is entirely well-defined independent of the
   application. Therefore, Subsection 2d requires that any
   application-supplied function or table used by this function must
   be optional: if the application does not supply it, the square
   root function must still compute square roots.)
These requirements apply to the modified work as a whole. If
identifiable sections of that work are not derived from the Library,
and can be reasonably considered independent and separate works in
themselves, then this License, and its terms, do not apply to those
sections when you distribute them as separate works. But when you
distribute the same sections as part of a whole which is a work based
on the Library, the distribution of the whole must be on the terms of
this License, whose permissions for other licensees extend to the
entire whole, and thus to each and every part regardless of who wrote
it.
Thus, it is not the intent of this section to claim rights or contest
your rights to work written entirely by you; rather, the intent is to
exercise the right to control the distribution of derivative or
collective works based on the Library.
In addition, mere aggregation of another work not based on the Library
with the Library (or with a work based on the Library) on a volume of
a storage or distribution medium does not bring the other work under
the scope of this License.
 3. You may opt to apply the terms of the ordinary GNU General Public
License instead of this License to a given copy of the Library. To do
this, you must alter all the notices that refer to this License, so
that they refer to the ordinary GNU General Public License, version 2,
instead of to this License. (If a newer version than version 2 of the
ordinary GNU General Public License has appeared, then you can specify
that version instead if you wish.) Do not make any other change in
these notices.
 Once this change is made in a given copy, it is irreversible for
that copy, so the ordinary GNU General Public License applies to all
subsequent copies and derivative works made from that copy.
 This option is useful when you wish to copy part of the code of
the Library into a program that is not a library.
 4. You may copy and distribute the Library (or a portion or
derivative of it, under Section 2) in object code or executable form
under the terms of Sections 1 and 2 above provided that you accompany
it with the complete corresponding machine-readable source code, which
must be distributed under the terms of Sections 1 and 2 above on a
medium customarily used for software interchange.
 If distribution of object code is made by offering access to copy
from a designated place, then offering equivalent access to copy the
source code from the same place satisfies the requirement to
distribute the source code, even though third parties are not
compelled to copy the source along with the object code.
 5. A program that contains no derivative of any portion of the
Library, but is designed to work with the Library by being compiled or
linked with it, is called a "work that uses the Library". Such a
work, in isolation, is not a derivative work of the Library, and
therefore falls outside the scope of this License.
 However, linking a "work that uses the Library" with the Library
creates an executable that is a derivative of the Library (because it
contains portions of the Library), rather than a "work that uses the
library". The executable is therefore covered by this License.
Section 6 states terms for distribution of such executables.
 When a "work that uses the Library" uses material from a header file
that is part of the Library, the object code for the work may be a
derivative work of the Library even though the source code is not.
Whether this is true is especially significant if the work can be
linked without the Library, or if the work is itself a library. The
threshold for this to be true is not precisely defined by law.
 If such an object file uses only numerical parameters, data
structure layouts and accessors, and small macros and small inline
functions (ten lines or less in length), then the use of the object
file is unrestricted, regardless of whether it is legally a derivative
work. (Executables containing this object code plus portions of the
Library will still fall under Section 6.)
 Otherwise, if the work is a derivative of the Library, you may
distribute the object code for the work under the terms of Section 6.
Any executables containing that work also fall under Section 6,
whether or not they are linked directly with the Library itself.
 6. As an exception to the Sections above, you may also combine or
link a "work that uses the Library" with the Library to produce a
work containing portions of the Library, and distribute that work
under terms of your choice, provided that the terms permit
modification of the work for the customer's own use and reverse
engineering for debugging such modifications.
 You must give prominent notice with each copy of the work that the
Library is used in it and that the Library and its use are covered by
this License. You must supply a copy of this License. If the work
during execution displays copyright notices, you must include the
copyright notice for the Library among them, as well as a reference
directing the user to the copy of this License. Also, you must do one
of these things:
   a) Accompany the work with the complete corresponding
   machine-readable source code for the Library including whatever
   changes were used in the work (which must be distributed under
   Sections 1 and 2 above); and, if the work is an executable linked
   with the Library, with the complete machine-readable "work that
   uses the Library", as object code and/or source code, so that the
   user can modify the Library and then relink to produce a modified
   executable containing the modified Library. (It is understood
   that the user who changes the contents of definitions files in the
   Library will not necessarily be able to recompile the application
   to use the modified definitions.)
   b) Use a suitable shared library mechanism for linking with the
   Library. A suitable mechanism is one that (1) uses at run time a
   copy of the library already present on the user's computer system,
   rather than copying library functions into the executable, and (2)
   will operate properly with a modified version of the library, if
   the user installs one, as long as the modified version is
   interface-compatible with the version that the work was made with.
   c) Accompany the work with a written offer, valid for at
   least three years, to give the same user the materials
   specified in Subsection 6a, above, for a charge no more
   than the cost of performing this distribution.
   d) If distribution of the work is made by offering access to copy
   from a designated place, offer equivalent access to copy the above
   specified materials from the same place.
   e) Verify that the user has already received a copy of these
   materials or that you have already sent this user a copy.
 For an executable, the required form of the "work that uses the
Library" must include any data and utility programs needed for
reproducing the executable from it. However, as a special exception,
the materials to be distributed need not include anything that is
normally distributed (in either source or binary form) with the major
components (compiler, kernel, and so on) of the operating system on
which the executable runs, unless that component itself accompanies
the executable.
 It may happen that this requirement contradicts the license
restrictions of other proprietary libraries that do not normally
accompany the operating system. Such a contradiction means you cannot
use both them and the Library together in an executable that you
distribute.
 7. You may place library facilities that are a work based on the
Library side-by-side in a single library together with other library
facilities not covered by this License, and distribute such a combined
library, provided that the separate distribution of the work based on
the Library and of the other library facilities is otherwise
permitted, and provided that you do these two things:
   a) Accompany the combined library with a copy of the same work
   based on the Library, uncombined with any other library
   facilities. This must be distributed under the terms of the
   Sections above.
   b) Give prominent notice with the combined library of the fact
   that part of it is a work based on the Library, and explaining
   where to find the accompanying uncombined form of the same work.
 8. You may not copy, modify, sublicense, link with, or distribute
the Library except as expressly provided under this License. Any
attempt otherwise to copy, modify, sublicense, link with, or
distribute the Library is void, and will automatically terminate your
rights under this License. However, parties who have received copies,
or rights, from you under this License will not have their licenses
terminated so long as such parties remain in full compliance.
 9. You are not required to accept this License, since you have not
signed it. However, nothing else grants you permission to modify or
distribute the Library or its derivative works. These actions are
prohibited by law if you do not accept this License. Therefore, by
modifying or distributing the Library (or any work based on the
Library), you indicate your acceptance of this License to do so, and
all its terms and conditions for copying, distributing or modifying
the Library or works based on it.
 10. Each time you redistribute the Library (or any work based on the
Library), the recipient automatically receives a license from the
original licensor to copy, distribute, link with or modify the Library
subject to these terms and conditions. You may not impose any further
restrictions on the recipients' exercise of the rights granted herein.
You are not responsible for enforcing compliance by third parties with
this License.
 11. If, as a consequence of a court judgment or allegation of patent
infringement or for any other reason (not limited to patent issues),
conditions are imposed on you (whether by court order, agreement or
otherwise) that contradict the conditions of this License, they do not
excuse you from the conditions of this License. If you cannot
distribute so as to satisfy simultaneously your obligations under this
License and any other pertinent obligations, then as a consequence you
may not distribute the Library at all. For example, if a patent
license would not permit royalty-free redistribution of the Library by
all those who receive copies directly or indirectly through you, then
the only way you could satisfy both it and this License would be to
refrain entirely from distribution of the Library.
If any portion of this section is held invalid or unenforceable under any
particular circumstance, the balance of the section is intended to apply,
and the section as a whole is intended to apply in other circumstances.
It is not the purpose of this section to induce you to infringe any
patents or other property right claims or to contest validity of any
such claims; this section has the sole purpose of protecting the
integrity of the free software distribution system which is
implemented by public license practices. Many people have made
generous contributions to the wide range of software distributed
through that system in reliance on consistent application of that
system; it is up to the author/donor to decide if he or she is willing
to distribute software through any other system and a licensee cannot
impose that choice.
This section is intended to make thoroughly clear what is believed to
be a consequence of the rest of this License.
 12. If the distribution and/or use of the Library is restricted in
certain countries either by patents or by copyrighted interfaces, the
original copyright holder who places the Library under this License may add
an explicit geographical distribution limitation excluding those countries,
so that distribution is permitted only in or among countries not thus
excluded. In such case, this License incorporates the limitation as if
written in the body of this License.
 13. The Free Software Foundation may publish revised and/or new
versions of the Lesser General Public License from time to time.
Such new versions will be similar in spirit to the present version,
but may differ in detail to address new problems or concerns.
Each version is given a distinguishing version number. If the Library
specifies a version number of this License which applies to it and
"any later version", you have the option of following the terms and
conditions either of that version or of any later version published by
the Free Software Foundation. If the Library does not specify a
license version number, you may choose any version ever published by
the Free Software Foundation.
 14. If you wish to incorporate parts of the Library into other free
programs whose distribution conditions are incompatible with these,
write to the author to ask for permission. For software which is
copyrighted by the Free Software Foundation, write to the Free
Software Foundation; we sometimes make exceptions for this. Our
decision will be guided by the two goals of preserving the free status
of all derivatives of our free software and of promoting the sharing
and reuse of software generally.
   NO WARRANTY
 15. BECAUSE THE LIBRARY IS LICENSED FREE OF CHARGE, THERE IS NO
WARRANTY FOR THE LIBRARY, TO THE EXTENT PERMITTED BY APPLICABLE LAW.
EXCEPT WHEN OTHERWISE STATED IN WRITING THE COPYRIGHT HOLDERS AND/OR
OTHER PARTIES PROVIDE THE LIBRARY "AS IS" WITHOUT WARRANTY OF ANY
KIND, EITHER EXPRESSED OR IMPLIED, INCLUDING, BUT NOT LIMITED TO, THE
IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A PARTICULAR
PURPOSE. THE ENTIRE RISK AS TO THE QUALITY AND PERFORMANCE OF THE
LIBRARY IS WITH YOU. SHOULD THE LIBRARY PROVE DEFECTIVE, YOU ASSUME
THE COST OF ALL NECESSARY SERVICING, REPAIR OR CORRECTION.
 16. IN NO EVENT UNLESS REQUIRED BY APPLICABLE LAW OR AGREED TO IN
WRITING WILL ANY COPYRIGHT HOLDER, OR ANY OTHER PARTY WHO MAY MODIFY
AND/OR REDISTRIBUTE THE LIBRARY AS PERMITTED ABOVE, BE LIABLE TO YOU
FOR DAMAGES, INCLUDING ANY GENERAL, SPECIAL, INCIDENTAL OR
CONSEQUENTIAL DAMAGES ARISING OUT OF THE USE OR INABILITY TO USE THE
LIBRARY (INCLUDING BUT NOT LIMITED TO LOSS OF DATA OR DATA BEING
RENDERED INACCURATE OR LOSSES SUSTAINED BY YOU OR THIRD PARTIES OR A
FAILURE OF THE LIBRARY TO OPERATE WITH ANY OTHER SOFTWARE), EVEN IF
SUCH HOLDER OR OTHER PARTY HAS BEEN ADVISED OF THE POSSIBILITY OF SUCH
DAMAGES.
    END OF TERMS AND CONDITIONS

        How to Apply These Terms to Your New Libraries
 If you develop a new library, and you want it to be of the greatest
possible use to the public, we recommend making it free software that
everyone can redistribute and change. You can do so by permitting
redistribution under these terms (or, alternatively, under the terms of the
ordinary General Public License).
 To apply these terms, attach the following notices to the library. It is
safest to attach them to the start of each source file to most effectively
convey the exclusion of warranty; and each file should have at least the
"copyright" line and a pointer to where the full notice is found.
   <one line to give the library's name and a brief idea of what it does.>
   Copyright (C) <year> <name of author>
   This library is free software; you can redistribute it and/or
   modify it under the terms of the GNU Lesser General Public
   License as published by the Free Software Foundation; either
   version 2.1 of the License, or (at your option) any later version.
   This library is distributed in the hope that it will be useful,
   but WITHOUT ANY WARRANTY; without even the implied warranty of
   MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the GNU
   Lesser General Public License for more details.
   You should have received a copy of the GNU Lesser General Public
   License along with this library; if not, write to the Free Software
   Foundation, Inc., 51 Franklin St, Fifth Floor, Boston, MA 02110-1301 USA
Also add information on how to contact you by electronic and paper mail.
You should also get your employer (if you work as a programmer) or your
school, if any, to sign a "copyright disclaimer" for the library, if
necessary. Here is a sample; alter the names:
 Yoyodyne, Inc., hereby disclaims all copyright interest in the
 library `Frob' (a library for tweaking knobs) written by James Random Hacker.
 <signature of Ty Coon>, 1 April 1990
 Ty Coon, President of Vice
That's all there is to it!